## Slide 1: Project Title : IOT Based Patient Health Monitoring on ESP32 Web Server
Course Teacher: Md. Shaoran Sayem
Lecturer
Department of Electrical and Electronic Engineering
SL # | Students ID | Students Name | Program | Section
1 | 22-46013-1 | MD. SHOHANUR RAHMAN SHOHAN | BSc in CSE | J
2 | 22-47006-1 | MD. ASHIKUZZAMAN ABIR | BSc in CSE | J
3 | 22-47010-1 | MD. JAHID HASAN | BSc in CSE | J
4 | 22-47018-1 | FARJANA YESMIN OPI | BSc in CSE | J
5 | 22-47019-1 | MD. ABU TOWSIF | BSc in CSE | J
6 | 22-47048-1 | A. F. M. RAFIUL HASSAN | BSc in CSE | J
Course Code: | COE3102 | Course Name: | MICROPROCESSOR AND EMBEDDED SYSTEMS

## Slide 2
Objectives ------------------------------------------------------------------- Slide (3)
Introduction ------------------------------------------------------------------------- Slide (4-5)
Literature Review ---------------------------------------------------------- Slide (6-8)
Working Method ----------------------------------------------------------- Slide (9-10)
Description of the Work ------------------------------------------------------ Slide
Results and Discussions ------------------------------------------------- Slide
Conclusions --------------------------------------------------------------------- Slide
Future Works ------------------------------------------------------------------------Slide
Outline of the Presentation

## Slide 3
Objectives of the Work
To develop a sensor interface
To implement a communication protocol
To incorporate data visualization
To analyze health data
To design an alerting mechanism
To simulate real-world scenarios
To test system reliability
To validate accuracy and effectiveness

## Slide 4
Introduction
Background information
Traditional healthcare monitoring often relies on periodic visits to healthcare facilities, which may not capture real-time health fluctuations
Remote patient monitoring has emerged as a promising solution to bridge this gap by allowing continuous monitoring of vital signs from the comfort of the patient's home
IoT technology offers a scalable and cost-effective approach to implement remote patient monitoring systems, enabling real-time data collection and analysis

## Slide 5
Introduction
Motivation
Enhanced Patient Care
Improved Access to Healthcare
Reduced Healthcare Costs
Empowering Patients
Research and Data Analysis

## Slide 6
Literature Review
Introduction to IoT in Healthcare
In recent years, the integration of IoT technology into healthcare systems has garnered significant attention for its potential to revolutionize patient monitoring. IoT-enabled systems facilitate remote monitoring of patient health parameters, offering real-time data collection and analysis for improved healthcare outcomes
The seamless integration of IoT technology into healthcare not only improves the quality of patient care but also reduces healthcare costs and enhances overall efficiency. IoT-enabled healthcare systems enable proactive intervention, personalized care delivery, and remote patient monitoring, transforming traditional healthcare practices.
Significance and potential of IoT to revolutionize
healthcare systems

## Slide 7
Literature Review
Existing Approaches in IoT-based Patient Health Monitoring
Cloud-based patient monitoring systems leverage platforms like Raspberry Pi to enable remote access to patient data for healthcare professionals. These systems facilitate seamless communication and collaboration, enhancing the efficiency and effectiveness of healthcare delivery.
Existing research has explored various approaches to IoT-based patient health monitoring, showcasing a range of innovative solutions. Wearable IoT devices equipped with sensors continuously monitor vital signs, while cloud-based patient monitoring systems enable remote access to patient data for healthcare professionals.
Wearable IoT devices equipped with sensors offer a convenient and accessible way to continuously monitor vital signs such as heart rate, blood pressure, and body temperature. These devices enable real-time monitoring of patient health parameters, facilitating timely intervention and personalized care delivery.

## Slide 8
Literature Review
Advancements in Microcontroller Technology
and Gap in Literature
Recent advancements in microcontroller technology, such as the ESP32 microcontroller, have opened new possibilities for remote patient monitoring. The ESP32 microcontroller offers built-in Wi-Fi and Bluetooth connectivity, enabling seamless data transmission and communication in patient monitoring systems
Example study:
"ESP32 Microcontroller-Based Remote Health Monitoring System" (Journal of Medical Internet Research, 2022)
The paper "ESP32 Microcontroller-Based Remote Health Monitoring System" showcases the potential of utilizing microcontrollers like the ESP32 for real-time health monitoring applications. This study highlights the capabilities of the ESP32 microcontroller in facilitating remote patient monitoring and data transmission

## Slide 9
Working Method
System Architecture
Working Principle
The IoT-based Patient Health Monitoring project utilizes ESP32 development kits to monitor vital signs like pulse rate, temperature, and SpO2 remotely. ESP32 serves as both sensor controller and server, enabling real-time data processing and transmission via Wi-Fi to a web server. Healthcare professionals can access patient data stored in a centralized database from smart devices anywhere. Real-time alerts notify of abnormalities, enhancing timely interventions. This integration addresses challenges in IoT-based healthcare monitoring, advancing its adoption in real-world settings.

## Slide 10
Working Method
Progress of work:
Wearable sensors continuously monitor vital signs (heart rate, temperature, SpO2).
The ESP32 development kit on the wearable device transmits the sensor data securely via Wi-Fi.
The data is received by a web server and stored in a centralized database.
Healthcare professionals can access patient data remotely through any smart device.
The system generates real-time alerts for any abnormal readings, enabling timely interventions.
This system offers remote patient monitoring, reducing in-person visits and improving healthcare efficiency.

## Slide 11
Description of the Components
ESP32 Microcontroller
Breadboard
DHT11 Humidity & Temperature Sensor
DS18B20 Temperature Sensor
MAX30100 Pulse Oximeter Sensor
Male To Male Jumper Wires

## Slide 12
Description of the Diagram
IoT Based Patient Health Monitoring on ESP32 Web Server
The ESP32-based Patient Health Monitoring System uses MAX30100, DHT11, and DS18B20 sensors to monitor vital health metrics like heart rate, temperature, and humidity. The MAX30100 connects to GPIO21 and GPIO22 for heart rate and oxygen saturation readings, DHT11 monitors ambient temperature and humidity, and DS18B20 provides additional temperature data for effective healthcare management.

## Slide 13
Results and Discussions
Results
The ESP32 successfully connects to the designated Wi-Fi network, and upon successful connection, it obtains an IP address, which is displayed on the serial monitor.
The system accurately measures and displays various health parameters, including room temperature, room humidity, heart rate (BPM), blood oxygen level (SpO2), and body temperature. These readings are obtained using the MAX30100 pulse oximeter sensor, DHT11 humidity & temperature sensor, and DS18B20 temperature sensor.

## Slide 14
Results and Discussions
Results
Upon entering the IP address of the ESP32 into a web browser, a user-friendly web page is displayed. This page showcases the real-time health status of the patient, making it convenient for caregivers or medical professionals to monitor remotely.
The system is compatible with mobile devices, allowing users to access the patient's health status via a web browser on their smartphones or tablets.

## Slide 15
Results and Discussions
Discussions
The accuracy and reliability of the sensor readings are crucial for effective patient monitoring. The MAX30100 pulse oximeter sensor, DHT11 humidity & temperature sensor, and DS18B20 temperature sensor are chosen for their precision and consistency in measuring vital health parameters.
The ability to monitor patient health status in real-time is a significant advantage of this IoT-based system. Caregivers or medical professionals can promptly respond to any abnormalities or emergencies based on the live data provided by the system.
By hosting the health monitoring interface on a web server, the system ensures accessibility from any device with a web browser and internet connection. This accessibility enhances convenience for caregivers and enables remote monitoring of patients, even from a distance.

## Slide 16
Results and Discussions
Discussions
The user interface of the web page is designed to be intuitive and easy to understand. Clear and concise presentation of health parameters facilitates quick interpretation of data, enabling efficient decision-making by caregivers or medical professionals.
The system can be scaled up to accommodate additional features or sensors for comprehensive patient monitoring. Future enhancements may include integration with mobile applications, data analytics for trend analysis, and alerts/notifications for critical health conditions.

## Slide 17
Conclusions
Conclude with in 1-2 slides

## Slide 18
List your future works that you want to present during your final presentation in 1 slide.
Future Scopes

## Slide 19: Thanks for listening our presentation….
?